## Slide 1: Spacecraft Formation Flying Using Sliding Mode Control
Maggie Lawn
Air Force Research Laboratory Mentors/Collaborators:
Chau Ton and Morgan Baldwin

## Slide 2: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 3: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment
Notes: “formation flying”: two or more satellites that have to track and maintain a desired relative trajectory and/or a relative orientation

## Slide 4: Formation Flying
Benefits:
  Robustness to faults
  Versatility
  Cost
Past and planned missions using formation flying:
  Earth science missions: CLUSTER, GRACE, and TanDEM-X
  Space science missions: MMS, Stellar Imager, EXO-S
  Technology demonstration missions: PRISMA
Notes: CLUSTER uses a four-satellite formation to study the interactions between solar wind and the Earth’s magnetic field [1]. The GRACE mission uses two identical satellites to develop a high-fidelity model of Earth’s gravitational field [2]. TanDEM-X is a two-satellite mission for the generation of a high-fidelity digital elevation model of the surface of the Earth [3]. MMS uses four satellites in a tetrahedral formation to study the Earth’s magnetosphere [4]. Stellar Imager is a space-based ultraviolet/optical interferometer which uses a formation of 20+ small mirror satellites and a chief hub to study solar and stellar magnetic activity [5]. EXO-S is a two-satellite space-based telescope for the discovery and study of planets [6]. PRISMA is a technology demonstration mission using 2 satellites to qualify formation flying and rendezvous sensors and software

## Slide 5: Robust Control for Formation Flying
Multiple satellite system dynamics models can be complex
Simplified models are less accurate
Thrust and parametric uncertainties due to long-term operations or hazardous conditions
Notes: Why Use?
to guarantee formation fidelity via adequate formation control and stability without overtaxing onboard processing power, robust control algorithms can be used compensate for uncertainty and improve performanc

## Slide 6: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 7: Sliding Mode Control
Popular due to design simplicity and robustness to disturbances
2 steps:
  Design of sliding variable
  Choice of control to drive dynamics to sliding surface
Many sliding variable and control technique pairs exist

## Slide 8: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 9: Objective
Apply novel nonsingular terminal sliding mode controller to spacecraft formation flying
Prove robustness to uncertainty and disturbance
Present simulation and experiment results

## Slide 10: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 11: Dynamics
2 satellites, called “chief” and “deputy”
Assumptions: circular chief orbit and small separation distance between satellites
Clohessy-Wiltshire equations can be used to describe the relative motion
Notes: where is the chief’s orbital rate; , , and are the control inputs; and , , and are the matched disturbances in the LVLH directions
where 𝑛 is the chief’s orbital rate; 𝑢_𝑥, 𝑢_𝑦, and 𝑢_𝑧 are the control inputs; and 𝑑_𝑥, 𝑑_𝑦, and 𝑑_𝑧 are the matched disturbances in the LVLH directions

## Slide 12: Dynamics
Local Vertical Local Horizontal
Reference Frame

## Slide 13: Dynamics
  where
.

## Slide 14: Dynamics
Assumptions:
  can be written as where are commanded control inputs, are multiplicative control errors , and have known upper bound less than
  have known upper bounds
  can be written as where is the known nominal vector and has a known upper bound less than
Notes: Control errors – b is approximately equal to 1, represents mass error or thrust error, represents thrust noise
Disturbances – unmodeled dynamics (e.g. perturbations)
Model errors
Control errors – b is approximately equal to 1, represents mass error or thrust error, 𝛿𝑢 represents thrust noise
Disturbances – unmodeled dynamics (e.g. perturbations)
Model errors

## Slide 15: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 16: Classical Sliding Surface
Sliding variable:
Time derivative of :
Where
  , where
Notes: is the difference between the reference (desired) and true trajectories
is the desired trajectory
Design a control structure to guarantee as
𝜀(𝑡) is the difference between the reference (desired) and true trajectories
𝑥_𝑟𝑒𝑓 is the desired trajectory
Design a control structure to guarantee 𝜀_𝑥 (𝑡)→0 as 𝑡→∞

## Slide 17: Classical Sliding Surface
Assumptions:
Desired trajectory and its first and second derivatives are bounded by known positive constants ,

## Slide 18: Classical Sliding Surface
Solution:
When dynamics slide on surface , exponentially

## Slide 19: Classical Sliding Surface
To guarantee convergence of and to zero, and remain at 0
When
When

## Slide 20: Classical Sliding Surface
First control choice:
Again,
  Where
Therefore,

## Slide 21: Classical Sliding Surface
Where
Based on assumptions, is bounded above as
Gain is designed to satisfy the inequality
Notes: Since is always greater than , will always be opposite in sign to , thus, the surface can be reached anywhere. Once the states are on the sliding surface , and exponentially decays to zero.
Since 𝑘_𝑥 is always greater than (𝐹_𝑥 ) ̅, 𝜎 ̇ will always be opposite in sign to 𝜎_𝑥, thus, the surface 𝜎_𝑥=0 can be reached anywhere. Once the states are on the sliding surface 𝜎_𝑥=0, and 𝜀_𝑥 exponentially decays to zero.

## Slide 22: Classical Sliding Surface
Potential trajectory:

## Slide 23: Classical Sliding Surface
Previous control structure contains term, potentially increasing required control magnitude larger than the necessary value
Alternative control choice:

## Slide 24: Classical Sliding Surface
*
(2)
*
(1)
*
(3)
Potential Trajectory:

## Slide 25: Classical Sliding Surface
(1)
, so
until surface is reached
if undisturbed, will slide on surface
*
(2)
*
(1)
*
(3)

## Slide 26: Classical Sliding Surface
(2)
negative disturbance forces system away from surface
.
may be too small to compensate for and
If , push the trajectory further from surface
trajectory will eventually impact the surface again
*
(2)
*
(1)
*
(3)

## Slide 27: Classical Sliding Surface
(3)
In region where
Oscillate to origin as in previous method
*
(2)
*
(1)
*
(3)
Notes: Spiraling effect continues until in region where …

## Slide 28: Classical Sliding Surface
Advantages:
  Does not require in control structure (potentially lower magnitude)
  does converge to in finite time exponential convergence of
Disadvantages:
  Potentially takes longer to converge

## Slide 29: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 30: Alternative Sliding Surfaces
When
Discontinuity leads to
Notes: When is large, does not include the term. Additionally, the state exponential convergence property is maintained. However, when the discontinuity implies that .
When 𝜀_𝑥 is large, 𝜎 ̇_𝑥 does not include the 𝜀 ̇_𝑥 term. Additionally, the state (𝜀_𝑥,𝜀 ̇_𝑥 ) exponential convergence property is maintained. However, when 𝜀_𝑥=𝐿 the discontinuity implies that 𝑑/𝑑𝑡 𝑠𝑎𝑡(𝜀_𝑥 )=∞.

## Slide 31: Alternative Sliding Surfaces
Eliminates discontinuity
Non-exponential convergence

## Slide 32: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 33: Nonsingular Terminal Sliding Surface
and odd integers
Notes: regardless of the sign of , the function is always positive because the exponential function is always positive and the exponents on can be evaluated as and where and are both positive integers.
Venkataraman, Control of Nonlinear Systems Using Terminal Sliding Modes, 1993
regardless of the sign of 𝜀 ̇_𝑥, the function 𝑔(𝜀 ̇_𝑥 ) is always positive because the exponential function is always positive and the exponents on 𝜀 ̇_𝑥 can be evaluated as 𝜀 ̇_𝑥^(((𝑚_1+𝑚_2 ))/𝑚_1 ) and 𝜀 ̇_𝑥^(((𝑚_2−𝑚_1 ))/𝑚_1 ) where (𝑚_1+𝑚_2 ) and (𝑚_2−𝑚_1 ) are both positive integers.
Venkataraman, Control of Nonlinear Systems Using Terminal Sliding Modes, 1993

## Slide 34: Nonsingular Terminal Sliding Surface
Notes: regardless of the sign of , the function is always positive because the exponential function is always positive and the exponents on can be evaluated as and where and are both positive integers.
Venkataraman, Control of Nonlinear Systems Using Terminal Sliding Modes, 1993
regardless of the sign of 𝜀 ̇_𝑥, the function 𝑔(𝜀 ̇_𝑥 ) is always positive because the exponential function is always positive and the exponents on 𝜀 ̇_𝑥 can be evaluated as 𝜀 ̇_𝑥^(((𝑚_1+𝑚_2 ))/𝑚_1 ) and 𝜀 ̇_𝑥^(((𝑚_2−𝑚_1 ))/𝑚_1 ) where (𝑚_1+𝑚_2 ) and (𝑚_2−𝑚_1 ) are both positive integers.
Venkataraman, Control of Nonlinear Systems Using Terminal Sliding Modes, 1993

## Slide 35: Nonsingular Terminal Sliding Surface
Control input:
Does not require subtraction of a term

## Slide 36: Nonsingular Terminal Sliding Surface
Potential Trajectory:
*
(1)
(2)
*

## Slide 37: Nonsingular Terminal Sliding Surface
(1)
, so
until surface is reached
*
(1)
(2)
*

## Slide 38: Nonsingular Terminal Sliding Surface
(2)
negative disturbance forces system away from surface
can be designed such that immediately dominates
system will slide on the surface, ensuring that
*
(1)
(2)
*
Notes: a smaller control magnitude can still guarantee rapid convergence

## Slide 39: Nonsingular Terminal Sliding Surface
Additional benefits:
  Finite time convergence of due to selection of
  Four constants (i.e. and ) can be tuned to yield desired performance characteristics
  Use control that does not subtract term
  No singularity as introduced in other attempts to avoid subtracting term
Notes: as opposed to the linear surface with single constant
as opposed to the linear surface with single constant 𝛼

## Slide 40: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment
Notes: In this section, it will be shown through simulations that the nonsingular terminal sliding mode controller can quickly and effectively force the system to match a desired set of reference dynamics in finite time in the presence of exogenous disturbance and uncertainty in the control input.

## Slide 41: Simulations
Propagated 2 satellites’ nonlinear equations of motion separately
  In Earth centered inertial (ECI) frame
  Included J2 perturbation
Calculated x, y, and z components at each time step for computation of control inputs
Notes: The satellites’ nonlinear equations of motion, which included the J2 perturbation, were propagated in Earth-centered inertial (ECI) frame separately, and the LVLH components were calculated at each time step for use in the computation of control components.

## Slide 42: Simulations
Initial conditions and parameters
  Chief initial orbital elements:
  Initial relative state:
  Control parameters:
a (km) | e (dim) | i (dim) | (rad) | (rad) | (rad)
+300 | 0.1 | 0 |  |  | 0
a (km) | e (dim) | i (dim) |  |  | 
 | 0.1 | 0 |  |  | 0
(km) | (km) | (km) | (km/s) | (km/s) | (km/s)
10 | 5 | 5 | 0 | 0 | 0
10 | 5 | 5 | 0 | 0 | 0
(dim) | (dim) | (dim) | (N)
0.1 | 3 | 5 | 1.0
0.1 | 3 | 5 | 1.0
Notes: chaser satellite is assumed to have 1 kg unit mass

## Slide 43: Simulations
Error magnitudes:
  Disturbances:
  Thrust error: multiplicative () and noise ()
Disturbance () | (dim) | (N)
0.01 | 0.9 | 0.1
0.01 | 0.9 | 0.1
Notes: Both the disturbance and thrust noise () are multiplied my a normally distributed random value at each timestep in the simulation.
Both the disturbance and thrust noise (𝛿𝑢) are multiplied my a normally distributed random value at each timestep in the simulation.

## Slide 44: Simulations
Relative orbit components
Satellite trajectories in ECI frame
Notes: Dynamics propagated for span of 1 chief orbit (5431 sec).
Lvlh components with reference trajectory
Chief and chaser trajectories in ECI
Closely tracks reference

## Slide 45: Simulations
Error in relative orbit components,
Sliding variable components,
Notes: Tracking error.
Sliding variable over time.
Sliding variable goes to zero, causing the tracking error to go to zero
Dynamics track reference to within a few meters over the span of a single orbit

## Slide 46: Simulations
Control input components, u
Total over one orbit
Notes: Control input over time as it adapts to uncertainty and external disturbance
Total delta-V

## Slide 47: Simulations
Error magnitude was then varied to determine the range of values that can be compensated by the controller
Maximum error for each error type still resulting in convergence of x, y, and z:
Disturbance () | (dim) | (N)
0 – 0.05 | 0.75 - 1 | 0 - 0.2
0 – 0.05 | 0.75 - 1 | 0 - 0.2

## Slide 48
When errors are combined, convergence is achieved over a smaller range of error magnitudes
Convergence of sampled error combinations
Simulations
Notes: Combinations of errors sampled linearly along the range given in TABLE IV were applied to the simulation. Figure 12 shows the points on that range which result in convergence. Where points are missing from the sampled pattern, the combined errors resulted in non-convergence.

## Slide 49: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 50: Conclusions
Nonsingular terminal sliding mode control scheme is effective for control of a formation flying satellite system with a range of disturbances and uncertainties
Simulation results demonstrate successful performance
Discontinuous control function is difficult and expensive for onboard implementation

## Slide 51: Thank you. Questions?
Maggie Lawn

## Slide 52: Outline
Introduction to Formation Flying
Introduction to Sliding Mode Control
Objective of Project
Dynamics Model
Classical Sliding Surface
Alternative Sliding Surfaces
Nonsingular Terminal Sliding Surface
Simulations
Conclusions
Experiment

## Slide 53: Experiment
Simulate orbital motion of the spacecraft in the plane
Dynamics were scaled down to the lab frame and used to obtain the wheel velocity and command inputs
  1 orbital period in the spacecraft frame = 60s in the lab frame
  1km in the spacecraft frame = 1m in the lab frame
Control parameters:
(dim) | (dim) | (dim) | (N)
0.1 | 3 | 5 | 1.0
0.1 | 3 | 5 | 1.0
Notes: To demonstrate the effectiveness of the proposed control structure, an experiment is carried out with an omni-directional robot to simulate spacecraft dynamics.
the disturbance and parametric uncertainty were due to imperfection on the floor, e.g. bumps, and uncertainty in the wheel model, respectively.

## Slide 54
Robot’s trajectory with desired trajectory
Experiment

## Slide 55: Experiment
Robot’s position error
Robot’s velocity error
Notes: all the error goes to zero in finite and remains at zero in the presence of uncertainty and disturbance

## Slide 56: Experiment
Sliding variable evolution over time
Robot’s commanded control input
Notes: Sliding variable goes to zero, causing the tracking error to go to zero

## Slide 57: Proof
Lyapunov candidate function:
  Where

## Slide 58: Proof
From definition of ,
  when
Hence when
Notes: is a design choice, as is and and .
𝑐_3 is a design choice, as is 𝑐_2 and 𝑚_1 and 𝑚_2.

## Slide 59: Proof
When ,
Error dynamics reduce to
Proof in A. Goodyear, P. Christophe, P. Jean, Z. Costantinos, B. Morgan, I. Kolmanovsky, "Hardware implementation of Model Predictive Control for relative motion maneuvering," American Control Conference (ACC), 2015. IEEE, 2015.
  When the sign of the acceleration is equivalent to
  Hence, the line is an unattractive set
  Therefore, the surface can be reached everywhere

## Slide 60: Robot Details
A. Goodyear, P. Christophe, P. Jean, Z. Costantinos, B. Morgan, I. Kolmanovsky, "Hardware implementation of Model Predictive Control for relative motion maneuvering," American Control Conference (ACC), 2015. IEEE, 2015.
time-varying position of the robot with respect to the inertial lab frame was measured using VICON Motion Capture Systems
control algorithm is developed in Simulink, which used auto code generation to embed the algorithm onto the Beaglebone Black
The Beaglebone Black receives the position of the robot in the lab frame and send the wheel command control signal to the robot
All the calculations are performed on the Beaglebone Black. This hardware is chosen due to its computation limitation similar to those on small spacecraft

## Slide 61: Benefits to SMC
dynamic behavior of the system may be tailored by the particular choice of the sliding function
closed loop response becomes totally insensitive to some particular uncertainties. This principle extends to model parameter uncertainties, disturbance and nonlinearity that are bounded
From a practical point of view SMC allows for controlling nonlinear processes subject to external disturbances and heavy model uncertainties